## Slide 1: Robotics & Control 2
Cristian Lorenzi
Filippo Gottardo
Giulia Pegoraro
Edoardo Di Pietrantonio

## Slide 2: THE PROBLEM
3 mobile robotic agents should agree on a rendez-vous point and when in proximity of such point, they start a tracking task over a circular trajectory centered in the rendez-vous point.
SCENARIO SPECIFICS
All agents are unicycles;
All agents are independent from each other;
ADDITIONAL CONSTRAINTS
Agents live in a 2D grid 12x12;
Initial conditions of the agents can be randomly chosen (both position and orientation);
The final target trajectory is a circle of radius 1;
The proximity circle radius is 4;

## Slide 3: SOLUTION APPROACH
THREE STEPS PROCEDURE:
Consensus - before moving
Regulation – until proximity to rendez-vouz point
Tracking – until the end of the simulation
This algorithm is applied to each agent INDEPENDENTLY.
REGULATION CONTROL will be validated before applying it to the final solution system.
TRACKING CONTROL will be implemented using different control strategies:
- Linearization of state error dynamics
- Non-linear controller of state error dynamics
- Feedback linearization based on a reference point on the sagittal axis
- Feedback linearization based on second order derivatives
Each one will be validated using the same methodologies and compared in order to draw final conclusions.

## Slide 4: CONSENSUS
The adopted strategy is AVERAGE CONSENSUS.
Consensus is computed before starting the control action and does not change over time

## Slide 5: CONSENSUS
HOW DO WE CHOOSE THE P MATRIX ?
We need Primitive and doubly stochastic P
CONSENSUS DYNAMICS where is the state of the system, containing the position of all the agents
Average consensus in one step
Average consensus

## Slide 6: REGULATION - CARTESIAN
GOAL: reach the desired target configuration
q = [0, 0, ?]

## Slide 7: REGULATION - POSTURE
GOAL: reach the desired target configuration
q = [0, 0, 0]
TWO OPTIONS:
Control Law with singularity at the origin
Control Law without singularity at the origin
In our scenario we will implement the latter

## Slide 8: REGULATION - POSTURE
Desired behaviour is accomplished since we reach consensus point with final orientation equal to zero and at most the trajectory presents one backup manuever.

## Slide 9: CONTROLLER SWITCH
How do we switch between posture regulation and tracking control ?
IMPLEMENTATION PROBLEM:
Posture regulation and tracking control are two different subsystems in Simulink !
The tracking subsytem must inherit initial conditions from the last iteration of the regulation subsystem.
Transition between controllers must be smooth. We should avoid sudden changes in orientation and velocity.

## Slide 10: CONTROLLER SWITCH
EXAMPLE OF NON SMOOTH TRANSITION
THIS CAN BE AVOIDED WITH PROPER TUNING

## Slide 11: TESTS & EVALUATION PROCEDURE
CONVERGENCE TEST:
SMOOTHNESS TEST:
SENSITIVITY TEST:
PROXIMITY TEST:
Compare for different tracking strategies
Evaluate the agents’ path smoothness
How robust is the controller to gain changes

## Slide 12: ERROR CHECK BLOCK
For easy and automatic evaluation of controller functionality a simple block is implemented:
Convergence flag
We set

## Slide 13: CONVERGENCE AND PROXIMITY TESTS
1
Perform N simulations starting from random initial positions and for each simulation collect the output of error check block
2
Convergence score is given by the following equation:
3
Compute the average time to reach proper tracking and average distance from desired trajectory at flag switch
ONLY USE SUCCESSFUL RUNS!

## Slide 14: SENSITIVITY TEST
1
Perform N simulations
starting from random initial positions
slightly changing control parameters
for each simulation collect the output of
error check block
2
Convergence score is given by the following equation:

## Slide 15: SMOOTHNESS TEST
Since the description of «smooth path» can be very generic and its definition can become cumbersome and hard to automate, the evaluation of this property is performed manually for a small number of runs.
Path characteristics considered for the evaluation:
Inversion manouvers
Sudden changes to speeds
Discontinuities (due to improper gain tuning)

## Slide 16: TRACKING: CIRCULAR TRAJECTORY
Digitare l'equazione qui.
(xC , yC)
pd = (xd , yd)
CENTER
RADIUS
FREQUENCY
TRAJECTORY
,

## Slide 17: LINEAR CONTROLLER - IMPLEMENTATION
We expect asymptotically stable control law from application of Barbalat’s Lemma and since we have a circular trajectory to follow
CONTROL LAW
CONTROL GAINS
INPUT TRANSFORMATION

## Slide 18: LINEAR CONTROLLER - RESULTS
CONVERGENCE TEST
90%
SENSITIVITY TEST
86.67%
PROXIMITY TEST (avg norm distance)
0.240

## Slide 19: LINEAR CONTROLLER - RESULTS

## Slide 20: LINEAR CONTROLLER – IMPLEMENTATION ISSUES
UNWRAP in differential flatness block for angle theta computation
DERIVATIVES computation in differential flatness block
ALPHA tuning via trial and error method

## Slide 21: THIS IS THE EXPLANATION – HIDDEN SLIDE
Unwrap: used to avid discontinuity in angle computation. Discontinuities lead to unexpected behaviour of the system.
First order high pass filter.
Large alphas increase the control action. Excessive control action leads to slow convergence time to the desired trajectory and more backup manuevers.

## Slide 22
We expect asymptotically stable control law from application of Barbalat’s Lemma
NON-LINEAR CONTROLLER - IMPLEMENTATION
INPUT TRANSFORMATION
CONTROL GAINS
CONTROL LAW

## Slide 23: NON-LINEAR CONTROLLER - RESULTS
CONVERGENCE TEST
100%
SENSITIVITY TEST
100%
PROXIMITY TEST (avg error)
0.235

## Slide 24: NON-LINEAR CONTROLLER - RESULTS

## Slide 25
We expect smooth trajectory and tuning flexibility, since we have decoupled dynamics and feedforward action
SAGITTAL CONTROLLER - IMPLEMENTATION
INPUT TRANSFORMATION
P2B TRANSFORMATION
CONTROL LAW

## Slide 26: SAGITTAL CONTROLLER - RESULTS
CONVERGENCE TEST
100%
SENSITIVITY TEST
99.33%
PROXIMITY TEST (avg error)
0.300

## Slide 27: SAGITTAL CONTROLLER - RESULTS

## Slide 28
We expect smooth trajectory and even more control flexibility
D. DERIVATIVE CONTROLLER - IMPLEMENTATION
P2Z TRANSFORMATION
CONTROL LAW
INPUT TRANSFORMATION

## Slide 29: D. DERIVATIVE CONTROLLER - RESULTS
CONVERGENCE TEST
94%
SENSITIVITY TEST
78%
PROXIMITY TEST (avg error)
0.262

## Slide 30: D. DERIVATIVE CONTROLLER - RESULTS

## Slide 31: D. DERIVATIVE CONTROLLER - ISSUES
DERIVATIVE of STATE
Continuous time block:
Instability issues, exploding values of derivative
First order high pass filter:
Filtering high frequency components and thus avoiding too sudden variations

## Slide 32: D. DERIVATIVE CONTROLLER - ISSUES
LINEAR VELOCITY
Linear velocity must be different from zero to ensure non singularity of the matrix
Solution: Set the minimum linear velocity to 1e-4

## Slide 33: CONTROLLER COMPARISON
 | LINEAR | NON-LINEAR | SAGITTAL | D.DERIVATIVE
TUNING | EASY | HARD | EASY | HARD
SMOOTHNESS | POOR | POOR | GOOD | GOOD
IMPL. ISSUES | FEW | FEW | FEW | MANY
CONV. TIME | 3.915 | 2.876 | 2.268 | 3.319
SENSITIVITY | MEDIUM | LOW | LOW | HIGH

## Slide 34: FINAL CONSIDERATIONS
 | PRO | CONS
LINEAR | Linear dynamics Poles allocation rule | Approximation around equilibrium Differential Flatness needed Stability only for specific conditions
NON-LINEAR | No approximation needed Robustness | Non-linear dynamics Differential Flatness needed
SAGITTAL | Decoupled dynamics No differential flatness Linear control law Feedforward action | Smooth desired trajectory Theta is not controllable Choice of parameter b
DOUBLE DERIVATIVES | Decoupled dynamics No differential flatness Linear control law Feedforward action | Relies on second order derivatives Constraint on linear velocity v Sensitivity