## Slide 1: Robotics and Control 2
Cristian Lorenzi, Filippo Gottardo, Giulia Pegoraro, Edoardo Di Pietrantonio

## Slide 2: THE PROBLEM
3 mobile robotic agents should agree on a rendez-vous point, then, when in proximity of such point, they start a tracking task over a circular trajectory.
SCENARIO SPECIFICS
All agents are unicycles;
All agents are independent from each other;
ADDITIONAL CONSTRAINTS
Agents live in a 2D grid 12x12;
Initial conditions of the agents can be randomly chosen (both position and orientation);
The final target trajectory is a circle of radius 1;
The proximity circle radius is 4 or 0.5;

## Slide 3: SOLUTION APPROACH
THREE STEPS PROCEDURE:
Consensus - before moving
Regulation – until proximity to rendez-vouz point
Tracking – until the end of the simulation
This algorithm is applied to each agent INDEPENDENTLY.
REGULATION CONTROL will be validated before applying it to the final solution system.
TRACKING CONTROL will be implemented using different control strategies:
Linearization of state error dynamics
Non-linear controller of state error dynamics
Feedback linearization based on a reference point on the sagittal axis
Feedback linearization based on second order derivatives
Each one will be validated using the same methodologies and compared in order to draw final conclusions.

## Slide 4: CONSENSUS
The consensus point is computed before any movement, based on the initial position of each agent.
The adopted strategy is AVERAGE CONSENSUS, meaning we compute the center of mass of the agents as rendez-vous point.
MISSING IMAGE
Future improvement - Consensus could be dynamically computed at every step of the iteration until every agent is in its proximity.

## Slide 5: REGULATION - CARTESIAN
GOAL: reach the desired target configuration
q = [0, 0, ?]

## Slide 6: REGULATION - POSTURE
GOAL: reach the desired target configuration
q = [0, 0, 0]
TWO OPTIONS:
Control Law with singularity at the origin
Control Law without singularity at the origin
In our scenario we will implement the latter

## Slide 7: REGULATION - POSTURE
Desired behaviour is accomplished since we reach consensus point with final orientation equal to zero and at most the trajectory presents one backup manuever.

## Slide 8: CONTROLLER SWITCH
How do we switch between posture regulation and tracking control?
A simulink block is responsible for checking if we are inside a fixed proximity radius, in which case it switches controller
Proximity radius is set to 4
IMPLEMENTATION PROBLEMS
Posture regulation and tracking control are two different subsystems in Simulink.
The tracking subsytem must inherit initial conditions from the last iteration of the regulation subsystem.
Transition between controllers must be smooth. We should avoid sudden changes in orientation and velocity.

## Slide 9: TESTING PROCEDURE
CONVERGENCE TEST – tests if the controller strategy works and how quickly the agents move to the desired position/trajectory
SMOOTHNESS TEST – tests the smoothness of the agents paths
SENSITIVITY TEST – tests the robustness of the controllers to small changes of gain values
PROXIMITY TEST – tests how close the agents are to the desired trajectory
Each test (except for the smoothness test) is automated via MatLab livescript.
The smoothness test was impossible to automate since the final results could only be interpreted by a human depending on his needs (trajectory path).
Each trajectory tracking controller was tested using this procedure.

## Slide 10: CONVERGENCE AND PROXIMITY TESTS
A Simulink Block named «Error Check> is responsible for:
Collecting the distance of the agent from the desired trajectory
Checking if the distance is below a given threshold, in that case we say that proper tracking is achieved.
The test is divided in steps:
Perform N simulations with random initial conditions and collect data from «Error Check» block
To compute the convergence score just verify how many times proper tracking is achieved over N simulations
If proper tracking is achieved proximity returns the distance from desired trajectory and the time needed to reach proper tracking

## Slide 11: LINEAR CONTROLLER - IMPLEMENTATION
We expect:
Asympatotically stable control law since the desired trajectory is circular
Backup manuevers

## Slide 12: LINEAR CONTROLLER - RESULTS
Smoothness image
CONVERGENCE TEST
94%
SENSITIVITY TEST
80/100
PROXIMITY TEST (avg error)
2.58

## Slide 13: LINEAR CONTROLLER – IMPLEMENTATION ISSUES
UNWRAP in differential flatness block for angle theta computation
DERIVATIVES computation in differential flatness block
ALPHA tuning via trial and error method

## Slide 14: THIS IS THE EXPLANATION – HIDDEN SLIDE
Unwrap: used to avid discontinuity in angle computation. Discontinuities lead to unexpected behaviour of the system.
Simulink continuous derivative block was used for derivaives computation in differential flatness block. Since the desired trajectory is extremely simple and does not present discontiuities this block is suitable for the task.
Large alphas increase the control action. Excessive control action leads to slow convergence time to desired trajectory and more backup manuevers

## Slide 15: NON-LINEAR CONTROLLER - IMPLEMENTATION
We expect:
Asympatotically stable control law since desired linear velocity and angular velocity are nevere convergin to zero together
Backup manuevers

## Slide 16: NON-LINEAR CONTROLLER - RESULTS
Smoothness image
CONVERGENCE TEST
94%
SENSITIVITY TEST
80/100
PROXIMITY TEST (avg error)
2.58

## Slide 17: SAGITTAL CONTROLLER- IMPLEMENTATION
We expect:
Asympatotically stable control law
Possible backup manuevers

## Slide 18: SAGITTAL CONTROLLER -IMPLEMENTATION
Controller scheme/formulas

## Slide 19: SAGITTAL CONTROLLER - RESULTS
Smoothness image
CONVERGENCE TEST
94%
SENSITIVITY TEST
80/100
PROXIMITY TEST (avg error)
2.58

## Slide 20: D. DERIVATIVE CONTROLLER - IMPLEMENTATION
We expect:
Asympatotically stable control law
No Backup manuevers since the system must always move to avoid singularity (linear velocity always different from 0)

## Slide 21: DOUBLE DERIVATIVE CONTROLLER - RESULTS
Smoothness image
CONVERGENCE TEST
94%
SENSITIVITY TEST
80/100
PROXIMITY TEST (avg error)
2.58

## Slide 22: D. DERIVATIVE CONTROLLER - IMPLEMENTATION
DERIVATIVE of STATE
Continuous time block:
Instability issues, exploding values of derivative
Discrete time derivative:
Helps to avoid explosion of derivative values, if combined with saturation blocks it gives an acceptable implementation

## Slide 23: CONTROLLER COMPARISON
TABLE OF RESULTS FOR COMPARISON

## Slide 24: FINAL CONSIDERATIONS
TABLE OF RESULTS FOR COMPARISON